## Slide 1: v4l2 capture example in C (Step by Step)
By Arash Golgol

## Slide 2: Agenda
The problem
A quick review of v4l2
Overview of solution

## Slide 3: The problem
Write C program which
  Capture single frame from webcam and save it
  Don’t use any library (e.g. opencv, gstreamer, libcamera, … )
Resources
  Check Linux man pages
  Check videodev2.h file
  Check v4l2 user space api documentation
  Check Streaming I/O example

## Slide 4: v4l2 overview
Kernel Space
User Space
Hardware
/dev/video0
ISP
I2C / SPI
master
Image Capture
DMA
Memory
v4l2
subdev
video buffer
ioctl ops
open()
close()
read()
write()
ioctl()
select()
mmap()
Notes: اهداف اصلی
عدم وابستگی بین درایورهای مختلف
ارایه یک واسط کاربری یکپارچه
شرایط بغلی بگیر در پایپلاین

## Slide 5: Solution materials
We only need C library
  open() , close(): Every other system calls need file descriptor
  select(): IO multiplexing and wait for frame to become ready
  mmap(): Map kernel space buffers (containing frames) into user space
  ioctl(): Configuration and control of v4l2 device
  write(): ??
And lot’s of effort 

## Slide 6: Capture process

## Slide 7: Overview
Open target camera device (e.g. /dev/video0)
Check it’s capabilities for capture and streaming (VIDIOC_QUERYCAP)
Check / Configure it’s frame size, pixel format, … (VIDIOC_G_FMT)
Request at least 3 buffer (VIDIOC_REQBUFS)
Query buffers information and map them (VIDIOC_QUERYBUF)
Enqueue buffers into driver queue (VIDIOC_QBUF)
Start streaming (VIDIOC_STREAMON)
Loop over
  Wait for buffer to become ready
  Dequeue buffer and process frame (VIDIOC_DQBUF)
  Enqueue buffer
Stop streaming, Unmap buffers and close camera device

## Slide 8: ioctl() simple example
process X
struct v4l2_capability
PAGE_OFFSET
kernel / User address space
(virtual)
kernel space
user space
struct v4l2_capability cap = {0};
int ret = ioctl(fd, VIDIOC_QUERYCAP, &cap);
struct v4l2_capability
int vidioc_querycap(… , struct v4l2_capability* cap);
copy_to_user(…, _IOC_SIZE(VIDIOC_QUERYCAP));
0x00000000

## Slide 9: ioctl() directions
_IOR(): Read data from kernel
_IOW(): Write data to kernel
_IOWR(): Combination of writing and reading
_IO(): Direction less (Without argument)
https://elixir.bootlin.com/linux/v6.16.5/source/include/uapi/linux/videodev2.h

## Slide 10: mmap() simple example
process X address space
(virtual)
Memory mapped file
TEXT
BSS
Regular file
(e.g image.raw)
offset
length
byte
addr
int fd = open(“image.raw”, O_RDONLY);
char* addr = mmap(
NULL, // hint for addr
length, // length of mapping
PROT_READ, // read only
MAP_PRIVATE, // not sharable
fd, // file descriptor
offset); // offset in file

## Slide 11: mmap() in v4l2 streaming mode
memory address space
(physical)
RAM
process X address space
(virtual)
Mapped segment
(vb2 buffers)
TEXT
BSS
MMU
cma
process X
vb2 buffers
0xFFFFFFFF
0x0
PAGE_OFFSET
kernel / User address space
(virtual)

## Slide 12: Mapping buffers
process X address space
(virtual)
buf0
TEXT
BSS
buf1
.addr
.len
.addr
.len
.addr
.len
.addr
.len
struct v4l2_frame_buff
.buffs
.count
struct v4l2_buffer_pool
buf2
buf3

## Slide 13: Capture
Buf 2
Buf 3
INPUT queue
Buf 0
Buf 1
OUTPUT queue
VIDIOC_DQBUF
VIDIOC_QBUF
Bridge Driver
(e.g atmel-isi)
vb2 framework
User space
Application
(e.g. Gstreamer)
Kernel space

## Slide 14: More information
Mastering Linux Device Driver Development by John Madieu (Chapter 9)
Linux V4L2 user API documentation: https://www.kernel.org/doc/html/v4.9/media/uapi/v4l/user-func.html